## Slide 1: GPU power variability in ML Systems
Ashwin Poduval
Rajesh Shashi Kumar
CS839: Adv. ML Systems, Spring 2022

## Slide 2: Outline
Problem Statement
Approach
Evaluation
Observations
Work in Progress

## Slide 3: Problem Statement
Power variation in systems can affect performance
  Black box system for renting resources
Problems of scale which is important in large ML training
  Exploiting scale central to the success of deep learning
  Aggressive utilization goals by occupants could lead to coupled effects

## Slide 4: Goals
Address systems reliability and explainability concerns
  Important for performance efficiency and cost of deployment
Develop intuition about GPU DVFS
Define stressmark for characterization of power variability in multi-GPU systems

## Slide 5: Approach
Define a strategy for data collection
Measurements:
Power variation!
Statistical variation
Effects to account for:
Spatial effects: Proximity of GPUs running workloads
  Systems today does not account for placement awareness
Temporal effects: High parallel utilization across GPUs at the same time

## Slide 6: Approach: Cont’d
Two fold experiment space:
Jetson: Controlled
  Understand performance variation with and without DVFS
CloudLab: Target system
  4 GPU Node, run ML workloads maximizing utilization

## Slide 7: RESNET + SGEMM

## Slide 8: SGEMM+RESNET+DistTranformer

## Slide 9: Evaluation
Workloads from the Nvidia DL repository:
Base:
SGEMM using cuBLAS
  (25536)2 matrix: 99.96% sm_efficiency
Noise:
RESNET50: Single node training, compute intensive
  Imagenet, BS128
Transformer: Data parallel training, memory intensive
  BS4096
CudaMemCpy: Synthetic data movement representation

## Slide 11: Experimental setup
https://www.wisc.cloudlab.us/portal/show-hardware.php?type=c4130 https://i.dell.com/sites/doccontent/shared-content/data-sheets/en/Documents/Dell-PowerEdge-C4130-Spec-Sheet.pdf
Notes: It’s imperative to go through the system configuration for a bit considering our analysis maybe affected by it. Though the redundant PSU makes the system resilient to external variations, but the dynamic interaction between components can lead to variation

## Slide 12: Experimental assumptions
Run profiling on all to ensure the same overheads across GPUs.
Variations can either be due to coupling in device physics or external factors
V100 does not support disabling autoboost
  Observed power envelope overshoot upto 300+25W in many cases

## Slide 14: Measurements
Primary components: Kernel runtime, Power
Second-order effects: Frequency, Temperature, Voltage

## Slide 15: Average kernel runtime for BASE(SGEMM) workload
SGEMM kernel x 100 reps
  Averaged over 2-4 runs
Key: Distinct pattern between GPUs perf even for small workload
GPU0 worst performer
GPU0,3 co-located?
3.5% variation in runtime (possibly more?)

## Slide 16: Average power consumption (RESNET50 + SGEMM)
GPU0 continues to be outlier
Pattern indicates variation is a measurable phenomenon
  Both RESNET/SGEMM 100% util
  Average lower for RESNET due to processing between iterations
  But variability more in RESNET
Key: Variability exists both within workload and between workloads

## Slide 17: Average power consumption across workloads

## Slide 18
GPU2
GPU1
GPU1
Case 1
Case 14
(a)
(b)
(c)
Notes: Please pardon me for data cramming here. Second order effect analysis is not trivial like the case of kernel runtimes

## Slide 19
(b) GPU2
(a) GPU1

## Slide 20: Pick a number between 0 and 3
Given 4 GPUs which one would you like to pick for a single node training?
Almost never a good idea to pick 0. Why?

## Slide 21: Idle conditions

## Slide 22: Scheduling makes a difference! Transformer + SGEMM (runs hot)

## Slide 24: Spatial interference! Closer GPUs running hotter

## Slide 25: What is volatile utilization? Not a measure of achieved_occupancy

## Slide 26: Work in Progress
Data correlation from all experiments
  Visualization is key to understand second-order effects
Formalize observations into device/application agnostic insights
Derive actions from current data to define future work
  Extensible beyond synthetic SGEMM through reusable stressmark
  Performance predictability: Effect of variation on tail latency
  Real-time profiling to guide mitigation
https://github.com/rajesh-s/mlsys-gpu-power-variability

## Slide 27: Backup slides

## Slide 28: Observed overshoot over 300W